## Slide 1
Prepare data (functional & anatomical) for analyses
Correct known sources of variation / noise
Speechlab Q: Why preprocessing in CONN?
a) CONN wraps SPM functionality: easy to use, transparent parallelization SCC cluster, QC
b) exactly same preprocessing steps are typically used for activation or connectivity analyses
c) new speechlab preprocessing & analysis pipeline uses CONN functionality
Setup
CONN17
Preprocessing

## Slide 2
Setup GUI
second-level
Results GUI
Denoising GUI
Setup GUI
Setup GUI
Setup GUI
Functional
& Structural
data
Denoise
Computes connectivity measures
Seed-based
connectivity
ROI-to-ROI
Graph
analyses
ICC
LCOR
GCOR
ALFF
Task-based
gPPI
Independent
Component
Analyses
Dynamic
connectivity
Preprocess
2nd-level
analyses
Experiment
design
ROIs
Removes physiological, artifacts, residual subject movement effects
Hypothesis testing
Population-level inferences
Prepares data
(realignment, unwarp? field-map correct? slice-timing correction? coregistration/ indirect normalization/ direct normalization? outlier identification, smoothing)
Imports data into CONN
first-level
Analyses GUI
QA
QA
QA

## Slide 3
Setup
Functional
& Structural
data
Preprocess functional/structural data
Enter raw Structural and Functional volumes
Define number of subjects and sessions/runs
Setup
Preprocess
Preprocessing pipeline:
Series of preprocessing steps (applied sequentially)

## Slide 4
1. MNI-space direct normalization
CONN’s default Preprocessing pipelines:
Realignment
Slice-timing
Functional Normalization
(direct)
Struct.nii
Funct.nii
Structural Segmentation & Normalization (direct)
uFunct.nii
auFunct.nii
wauFunct.nii
wStruct.nii
swauFunct.nii
Smoothing
+ wc1Struct.nii
wc2Struct.nii
wc3Struct.nii
rp_Funct.txt
art_regression_outliersauFunc.txt
Outlier detection
SPM prefix conventions
u : realign&unwarp
vdm write
r : realign (write)
coregister (write)
a : slice-timing correction
w : normalize (write)
s : smooth
c1 c2 c3 : gray/white/csf
c4 c5 c6 : bone/soft/air

## Slide 5
Realign & Unwarp
(+fieldmaps)
Slice-timing
Coregistration
Structural Segmentation & Normalization (indirect)
Struct.nii
Funct.nii
uFunct.nii
auFunct.nii
(auFunct.nii)
wStruct.nii
wauFunct.nii
swauFunct.nii
Smoothing
+ wc1Struct.nii
wc2Struct.nii
wc3Struct.nii
vdmFunct.nii
rp_Funct.txt
2. MNI-space indirect normalization FieldMaps available
CONN’s default Preprocessing pipelines:
art_regression_outliersFunc.txt
Outlier detection
(apply same deformation field to functional data)

## Slide 6
Realignment
Slice-timing
Coregistration
Struct.nii
Funct.nii
uFunct.nii
auFunct.nii
(auFunct.nii)
+ c1Struct.nii
c2Struct.nii
c3Struct.nii
Structural Segmentation
rp_Funct.txt
3. Subject-space
surface-based analyses
CONN’s default Preprocessing pipelines:
art_regression_outliersFunc.txt
Outlier detection

## Slide 7
Realignm & Unwarp (+fieldmaps)
Slice-timing
Coregistration
Structural Segmentation
Struct.nii
Funct.nii
uFunct.nii
auFunct.nii
(auFunct.nii)
+ c1Struct.nii
c2Struct.nii
c3Struct.nii
rp_Funct.txt
vdmFunct.nii
4. Subject-space
surface-based analyses / FieldMaps available
CONN’s default Preprocessing pipelines:
art_regression_outliersFunc.txt
Outlier detection

## Slide 8
conn_setup_preproc
Runs individual preprocessing steps
conn_setup_preproc(steps)
runs preprocessing pipeline (default_*) or one/multiple individual preprocessing steps (structural_* and functional_*). Valid step names are (enter as cell array to run multiple sequential steps):
PIPELINES:
default_mni : default MNI-space preprocessing pipeline
default_mniphase : same as default_mni but with vdm/phasemap information
default_ss : default subject-space preprocessing pipeline
default_ssphase : same as default_ss but with vdm/phasemap information
default_ssnl : same as default_ss but with non-linear coregistration
INDIVIDUAL STRUCTURAL STEPS:
structural_center : centers structural data to origin (0,0,0) coordinates
structural_manualorient : applies user-defined affine transformation to structural data
structural_manualspatialdef : applies user-defined spatial deformation to structural data
structural_normalize : structural normalization to MNI space
structural_segment : structural segmentation (Gray/White/CSF tissue classes)
structural_segment&normalize : structural unified normalization and segmentation
INDIVIDUAL FUNCTIONAL (or combined functional/structural) STEPS:
functional_art : functional identification of outlier scans (from motion displacement and global signal changes)
functional_center : centers functional data to origin (0,0,0) coordinates
functional_centertostruct : centers functional data to approximate structural-volume coordinates
functional_coregister_affine : functional affine coregistration to structural volumes
functional_coregister_nonlinear : functional non-linear coregistration to structural volumes
functional_manualorient : applies user-defined affine transformation to functional data
functional_manualspatialdef : applies user-defined spatial deformation to functional data
functional_motionmask : creates functional motion masks (mean BOLD signal spatial derivatives wrt motion parameters)
functional_normalize_direct : functional direct normalization
functional_normalize_indirect : functional indirect normalization (coregister to structural; normalize structural; apply same transformation to functionals)
functional_realign : functional realignment
functional_realign_noreslice : functional realignment without reslicing (applies transformation to source header files)
functional_realign&unwarp : functional realignment & unwarp (motion-by-inhomogeneity interactions)
functional_realign&unwarp&fieldmap : functional realignemnt & unwarp & inhomogeneity correction (from vdm/phasemap files)
functional_removescans : removes user-defined number of initial scans from functional data
functional_segment : functional segmentation (Gray/White/CSF tissue classes)
functional_segment&normalize_direct : functional direct unified normalization and segmentation
functional_segment&normalize_indirect : functional indirect unified normalization and segmentation (coregister to structural; normalize and segment structural; apply same transformation to functionals)
functional_slicetime : functional slice-timing correction
functional_smooth : functional spatial smoothing
conn_setup_preproc(steps,'param1_name',param1_value,'param2_name',param2_value,...)
defines additional non-default values for parameters specific to individual steps
fwhm : (functional_smooth) Smoothing factor (mm) [8]
coregtomean : (functional_coregister/segment/normalize) 0: use first volume; 1: use mean volume (computed during realignment); 2: use user-defined source volume (see Setup.coregsource_functionals field) [1]
sliceorder : (functional_slicetime) acquisition order (vector of indexes; 1=first slice in image; note: use cell array for subject-specific vectors)
alternatively sliceorder may also be defined as one of the following strings: 'ascending','descending','interleaved (middle-top)','interleaved (bottom-up)','interleaved (top-down)','interleaved (Siemens)','BIDS'
alternatively sliceorder may also be defined as a vector containing the acquisition time in milliseconds for each slice (e.g. for multi-band sequences)
ta : (functional_slicetime) acquisition time (TA) in seconds (used to determine slice times when sliceorder is defined by a vector of slice indexes; note: use vector for subject-specific values). Defaults to (1-1/nslices)*TR where nslices is the number of slices
art_thresholds : (functional_art) ART thresholds for identifying outlier scans
art_thresholds(1): threshold value for global-signal (z-value; default 5)
art_thresholds(2): threshold value for subject-motion (mm; default .9)
additional options: art_thresholds(3): 1/0 global-signal threshold based on scan-to-scan changes in global-BOLD measure (default 1)
art_thresholds(4): 1/0 subject-motion threshold based on scan-to-scan changes in subject-motion measure (default 1)
art_thresholds(5): 1/0 subject-motion threhsold based on composite-movement measure (default 1)
art_thresholds(6): 1/0 force interactive mode (ART gui) (default 0)
art_thresholds(7): [only when art_threshold(5)=0] subject-motion threshold based on rotation measure
art_thresholds(8): N number of initial scans to be flagged for removal (default 0)
note: when art_threshold(5)=0, art_threshold(2) defines the threshold based on the translation measure, and art_threhsold(7) defines the threshold based on the rotation measure; otherwise art_threshold(2) defines the (single) threshold based on the composite-motion measure
note: the default art_thresholds(1:2) [5 .9] values correspond to the "intermediate" (97th percentile) settings, to use the "conservative" (95th percentile) settings use [3 .5], to use the "liberal" (99th percentile) settings use [9 2] values instead
note: art needs subject-motion files to estimate possible outliers. If a 'realignment' first-level covariate exists it will load the subject-motion parameters from that first-level covariate; otherwise it will look for a rp_*.txt file (SPM format) in the same folder as the functional data
subject-motion files can be in any of the following formats: a) *.txt file (SPM format; three translation parameters in mm followed by pitch/roll/yaw in radians); b) *.par (FSL format; three Euler angles in radians followed by translation parameters in mm); c) *.siemens.txt (Siemens MotionDetectionParameter.txt format); d) *.deg.txt (same as SPM format but rotations in degrees instead of radians)
removescans : (functional_removescans) number of initial scans to remove
reorient : (functional/structural_manualorient) 3x3 or 4x4 transformation matrix or filename containing corresponding matrix
respatialdef : (functional/structural_manualspatialdef) nifti deformation file (e.g. y_*.nii or *seg_sn.mat files)
voxelsize_anat : (normalization) target voxel size for resliced anatomical volumes (mm) [1]
voxelsize_func : (normalization) target voxel size for resliced functional volumes (mm) [2]
boundingbox : (normalization) target bounding box for resliced volumes (mm) [-90,-126,-72;90,90,108]
interp : (normalization) target voxel interpolation method (0:nearest neighbor; 1:trilinear; 2 or higher:n-order spline) [4]
template_anat : (structural_normalize SPM8 only) anatomical template file for approximate coregistration [spm/template/T1.nii]
template_func : (functional_normalize SPM8 only) functional template file for normalization [spm/template/EPI.nii]
affreg : (normalization) affine registration before normalization ['mni']
tpm_template : (structural_segment, structural_segment&normalize in SPM8, and any segment/normalize option in SPM12) tissue probability map [spm/tpm/TPM.nii]
tpm_ngaus : (structural_segment, structural_segment&normalize in SPM8&SPM12) number of gaussians for each tissue probability map
conn_setup_preproc('steps')
returns the full list of valid preprocessing step names
>> help conn_setup_preproc

## Slide 9
CONN’s default Preprocessing pipelines:
Check your inputs
Before running an entire preprocessing pipeline or a subset of preprocessing steps make sure that the Structural/Functional data in your CONN project is set correctly (does it point to your raw or appropriately pre-processed data?)
Save / Load
Remember to save your own pipeline (particularly if you do not use one of the default pipelines) to more easily apply the same preprocessing steps to other subjects/datasets/studies
Folder conn/utils/preprocessingpipelines contains a few additional pipelines (e.g. no slice-timing correction for fast acquisitions, indirect normalization without FieldMaps, …)
Check your outputs
Visualize your structural/functional data, look for potential problems (Quality Assurance plots)

## Slide 10
Setup GUI
Setup GUI
second-level
Results GUI
Denoising GUI
Setup GUI
Setup GUI
Functional
& Structural
data
Denoise
Computes connectivity measures
Seed-based
connectivity
ROI-to-ROI
Graph
analyses
ICC
LCOR
GCOR
ALFF
Task-based
gPPI
Independent
Component
Analyses
Dynamic
connectivity
Preprocess
2nd-level
analyses
Experiment
design
ROIs
Removes physiological, artifacts, residual subject movement effects
Hypothesis testing
Population-level inferences
Prepares data
(realignment, unwarp? field-map correct? slice-timing correction? coregistration/ indirect normalization/ direct normalization? outlier identification, smoothing)
Imports data into CONN
first-level
Analyses GUI
QA
QA
QA
QA plots

## Slide 11
CONN’s
Quality Assurance plots
(preprocessing)
Movie of functional data with timeseries:
Global Signal scan-to-scan changes
Subject motion scan-to-scan displacement
Artifacts (outlier scans identified by ART)
OK: no visible outliers beyond those already identified by ART (bottom timeseres)
QA measures: QA_validscans: second-level covariate computing number of valid scans (discounting outlier scans)
QA artifacts
QA realignment
First- and last- acquisition across multiple sessions
OK: no visible differences between all images
QA measures: QA_maxmotion: second-level covariate computing maximum framewise displacement
Does your data show subject-motion or other visible artifacts?

## Slide 12
Overlay your functional data to MNI gray matter boundaries (25% gray matter MNI tissue probability maps)
OK: reasonably good match, particularly when averaged across all subjects. No visible consistent anatomical differences between subjects
QA measures: QA_Gray/white/CSF_vol
QA normalization functional
QA normalization structural
Overlay your ROIs onto an MNI template (e.g. gray/white/CSF ROIs: computed by preprocessing-pipeline segmentation step)
OK: white matter and CSF areas (particularly after erosion) do not overlap MNI template cortical gray matter regions
Is your data in MNI space?
Plot MNI-reference together with your functional/structural/ROI files
QA registration MNI reference
CONN’s
Quality Assurance plots
(preprocessing)

## Slide 13
CONN’s
Quality Assurance plots
(preprocessing)
Plot functional data with gray matter boundary (from ROIs: filled by preprocessing-pipeline segmentation step)
OK: reasonable match between functional and anatomical modalities
QA registration functional
QA registration structural
Are your functional and structural data properly co-registered?
Plot structural data with gray matter boundary (gray/white/CSF ROIs: computed by preprocessing-pipeline segmentation step)
OK: reasonable match between functional and anatomical modalities

## Slide 14
Additional info / references
SPM manual: http://www.fil.ion.ucl.ac.uk/spm/doc/manual.pdf
YouTube channels: Principles of fMRI (Martin Lindquist and Tor Wager)
  Andrew Jahn
SPM: www.fil.ion.ucl.ac.uk/spm
FSL: fsl.fmrib.ox.ac.uk/fsl
CONN: www.conn-toolbox.org
matlab: help conn_setup_preproc