## Slide 1: Chemical Analysis: Mass Spectrometry & Forensic Techniques
laurent hamels - Fotolia
Quality of Medical Products and Public Health
David A. Gaul
Georgia Institute of Technology

## Slide 2: Chemical Analysis
http://suzannevince.com

## Slide 3: Chemical Analysis
C H N O
C14H18N4O3
Benomyl (antifungal)
Trimethoprim (antibacterial)

## Slide 4: Chemistry & Packaging Simplify Definitions
Good Quality: Set of samples that did not fail chemical assays (content, dissolution, etc.) and packaging tests, if performed.
Degraded: genuine packaging + decreased quantity of correct API & chemical evidence of degradation.
Substandard: Samples with genuine packaging + incorrect quantity of correct API or other manufacturing defects.
Poor Quality: no genuine packaging to check + incorrect quantity of correct API (>zero %).
Falsified: Samples with fake packaging + right amount of API or none or “wrong API”. Also those samples with no genuine packaging available to compare with + wrong or no stated API. Definition could extend to excipients or coatings in more sophisticated cases.
wWARN AQ Surveyor. Paul Newton. Patricia Tabernero.

## Slide 5
Category A confirmatory | Category B screening | Category C presumptive
Mass Spectrometry | Capillary Electrophoresis | Color Tests
Infrared Spectrophotometry | Gas Chromatography | Fluorescence Spectroscopy
Nuclear Magnetic Resonance Spectroscopy | Ion Mobility Spectrometry | Immunoassay
Raman Spectroscopy | Liquid Chromatography | Melting Point
X-ray Diffraction Analysis | Microcrystalline Tests | Ultraviolet Spectrophotometry
 | Pharmaceutical Identifiers | 
 | Thin Layer Chromatography | 
 | Cannabis Only: Macroscopic Examination Microscopic Examination | 
SWGDRUG Recommendations 7.0
http://www.swgdrug.org/approved.htm
Minimum of 1x Category A, plus 1 more
http://www.astm.org/FULL_TEXT/E2329/HTML/E2329.htm
Standard Practice for Identification of Seized Drugs
ASTM E2329 & SWGDRUG
Notes: SCIENTIFIC WORKING GROUP FOR THE ANALYSIS OF SEIZED DRUGS (SWGDRUG) RECOMMENDATIONS

## Slide 6: Mass Spectrometry
We gain information on:
Elemental composition of matter
Structure of inorganic, organic and biological molecules
Qualitative and quantitative composition of complex mixtures
Structure and composition of solid surfaces
Isotopic ratios of atoms in samples
Application for routine chemical analysis since early 1940s
Structural identication in organic chemistry: NMR, MS, IR
Possibility to produce ions from non-volatile or thermally labile molecules since the 1980s  biological samples, including polypeptides, proteins, nucleic acids, even intact viruses!

## Slide 7: A Formal Definition
http://masspec.scripps.edu
Mass spectrometry is the art of measuring atoms and molecules to determine their molecular weight. Such mass or weight information is sometimes sufficient, frequently necessary, and always useful in determining the identity of a species. To practice this art one puts charge on the molecules of interest, i.e., the analyte, then measures how the trajectories of the resulting ions respond in vacuum to various combinations of electric and magnetic fields.
Clearly, the sine qua non of such a method is the conversion of neutral analyte molecules into ions. For small and simple species the ionization is readily carried by gas-phase encounters between the neutral molecules and electrons, photons, or other ions. In recent years, the efforts of many investigators have led to new techniques for producing ions of species too large and complex to be vaporized without substantial, even catastrophic, decomposition.
John Fenn, Chemistry Nobel Laureate 2002

## Slide 8
Mass Spectrometry – Essential Components
A mass spectrometer determines the mass of a molecule by measuring the mass-to-charge ratio (m/z) of its ion. Ions are generated by inducing either the loss or gain of a charge from a neutral species. Once formed, ions are electrostatically directed into a mass analyzer where they are separated according to m/z and finally detected. The result is a mass spectrum.
Ion Source
Detector
m/z Analyzer
IONS
Ions
Solids by
MALDI or
LSIMS
Vacuum
Computer/data system
Solids or
solutions
by ESI, APCI,
AP-MALDI
Fixed gases or
volatile liquids
by EI, CI, or FI

## Slide 9: Many Types of Ion Sources!
Electron Ionization
Fast Atom Bombardment
Electrospray Ionization
Matrix Assisted Laser Desorption/Ionization

## Slide 10: MALDI: Matrix-Assisted Laser Desorption/Ionization
Generally uses a UV laser.
IR MALDI is also used, but not that common.
Ions are formed by gas-phase proton transfer between the excited matrix ions and the analyte.

## Slide 11: Fenn’s First ESI Source Coupled to a Quadrupole MS

## Slide 12: Electrospray Ionization Process
Mass Spectrometry Reviews, 2001, 20, 362– 387.

## Slide 13: Mass Analyzer - Quadrupole
DC+RF
-(DC+RF)
-150V
DC Pole Bias Offset (equal in all poles and added to other voltages)
5
-500V
DC and RF between 100V and 1000V
Frequency: 1-4MHz
About 100 oscillations.
Z-direction
Filtering potentials

## Slide 14: Mass Analyzers – Time of Flight (TOF)
MALDI Linear TOF. Lower R. Very Sensitive.
MALDI Reflectron TOF. Higher R. Less Sensitive.

## Slide 15: Mass Analyzers - Orbitrap
Anal. Chem. 2000, 72, 1156-1162
Anal. Chem. 2006, 78, 2113-2120

## Slide 16: Mass Spectrum – 18 Amino Acids

## Slide 17: Tandem Mass (MS2) Spectrometry
MS experiments can also produce structural information by selecting a precursor ion (generated with soft ionization), activating these ions by collisions with a gas, and mass analyzing the fragments.
Two basic experiments:
  Tandem in time and tandem in space.

## Slide 18: Tandem MS in Time: MSn

## Slide 19: Tandem MS in Space
Roessner U., Beckles D. Plant Metabolic Networks 2009

## Slide 20: MSMS Phenylalanine
Journal of Cheminformatics 2013, 5:12

## Slide 21: Introduction to Chromatographic Separations (Skoog Ch. 26)
Introduction: - Frequently methods for chemical analysis are selective, but not highly specific - Separation of analyte from interferences required  Chromatography
General description: - Separation of chemically closely related components in a complex mixture - Sample transported in a mobile phase (gas, liquid, supercritical fluid) - Passes stationary phase fixed in column or on solid surface - Distribution equilibria of the analyte between mobile phase and stationary phase - Components strongly retained in the stationary phase move only slowly with the flow of the mobile phase, components weakly retained move rapidly - Components separate into zones (bands), which can be further analyzed

## Slide 22: Introduction to Chromatographic Separations
Notice that the analyte zones suffer broadening and dilution.
Therefore, when a chromatographic separation is performed, detectors need to be more sensitive!
Avoid separations if possible!
How do we decide if a separation is needed? Depends on selectivity and peak capacity of the detector.

## Slide 23: Chromatogram
Detector plots signal as function of time
Series of peaks obtained, called chromatogram
Qualitative and quantitative analysis possible
Migration rates and zone broadening simultaneously influence peak resolution
Zone broadening and analyte separation occur simultaneously! They are opposing effects

## Slide 24: Liquid Chromatography
Solvent A
Solvent B
HP pump
Injection system (autosampler or manual)
Chromatographic column
Detector
HPLC high performance liquid chromatography
- operating pressure below 6,000 psi
UPLC ultra performance liquid chromatography
- operating pressure below 15,000 psi
UHPLC ultra high performance liquid chromatography
- operating pressure below 20,000 psi

## Slide 25: HPLC Columns
Columns: - Stainless steel tubing - 10-30 cm length - Inner diameter: 1-10 mm - Particle size of packing: 2-10 µm - 40,000-60,000 plates per meter (much less than GC). UPLC: ~200,000
Guard columns are used before analytical column to remove particulate
matter, contaminants from solvent and components, which would
irreversibly bind to the stationary phase.

## Slide 26: HPLC Column Selection

## Slide 27: Instrumentation in HPLC
Mobile phase: - single solvent, constant composition = isocratic elution - gradually or stepwise varied composition (polarity) of mobile phase = gradient elution - Example shows isocratic 50:50 (v:v) (bottom) MeOH/Water in contrast to 40:60 with increased rate of MeOH by 8%/min (top)

## Slide 28: How to Reduce Band Broadening
In packed columns: reduce particle diameter.
HPLC
UHPLC

## Slide 29: LC Columns for Partition Chromatography
Normal-phase chromatography: highly polar stationary phase and relatively nonpolar solvent.
Reversed-phase chromatography: nonpolar stationary phase (e.g. bonded long-chain hydrocarbons, C4, C8, C18) and relatively polar solvent

## Slide 30: LCMS Data: Chromatogram and Mass Spectrum

## Slide 31: Laboratory Chemical Forensics The Cadillac of Chemical Detection Technology
www.codfin.org
Attribution/Sourcing:
Palynology
IR-MS

## Slide 32: Q Exactive HF

## Slide 33: Quantitation of Norfloxacin (antibacterial)
Mobile phase A – water with 0.1% formic acid
Mobile phase B – acetonitrile with 0.1% formic acid

## Slide 34: Quantitation of Norfloxacin
m/z
Relative Abundance
MzCloud
CE
MS2

## Slide 35: Quantitation of Norfloxacin
Chart: mg/100mg
| 0 | 20 | 40 | 60 | 80 | 100
mean | 0.014878 | 0.91457 | 2.0284 | 2.9812 | 3.7454 | 4.5506
Extracted Ion Chromatogram for Precursor and Transitions
Software: Skyline and Excel

## Slide 36: Laboratory Chemical Forensics The Cadillac of Chemical Detection Technology
www.codfin.org
Attribution/Sourcing:
Palynology
IR-MS

## Slide 37: Direct Analysis in Real Time-Mass Spectrometry (DART-MS)
Time-of-flight (TOF) mass spectrometer
DART ion source
No Sample Prep! Directly from solids

## Slide 38
DART Basics
M(s) M(g) (M+H)+(g)
DART Source
MS Inlet
Glass tube
Pv (T)
PA
(H2O)nH+ (H2O)n
Fernández, FM; Cody, RB; et al., ChemMedChem, 2006, 1, 702–705.
[M+H]+
[2M+H]+
Newton, PN; Fernández, FM; et al., PLoS Med., 2006, 3(6), e197

## Slide 39: DART-TOF MS
TMP2
RP
TMP1
RP
Ion Source
Ion Transportation
Analyser
Detection system
To the data collection system

## Slide 40
[Lumefantrine + H]+
[Artemether + NH4]+
[Dihydroartemisinin + NH4]+
[Piperaquine + H]+
[Artesunate + NH4]+
[Amodiaquine + H]+
Nigeria ACT Results: Genuine samples-On Going ACT Consortium Study in Enugu, Nigeria
Harparkash Kaur, Michael Green, Obinna Onwujekwe, Facundo Fernandez (& teams)
DART-TOF MS
DART-TOF MS
DART-TOF MS

## Slide 41
DART-TOF MS/MS
Fragmentation pattern indicates ciprofloxacin
[Ciprofloxacin + H]+ instead of artemether
DART-TOF MS
Nigeria ACT Results: Falsified samples (10/200)
Ciprofloxacin NIST MS/MS
antibacterial

## Slide 42
A
B
B
B
C
C
C
Falsified Emergency Contraceptive: Peru
David Jenkins (FHI), Facundo Fernandez (& teams)

## Slide 43: Laboratory Chemical Forensics The Cadillac of Chemical Detection Technology
www.codfin.org
Attribution/Sourcing:
Palynology
IR-MS

## Slide 44
Compact, low maintenance mass spectrometer (Waters QDa) with simple software.
Desktop sized system.
Energy-resolved in-source CID + DART Temperature ramping.
Spectral isotope profile fitting for elemental formula ID.
Benchtop DART-Single Quadrupole MS
Bernier et al., Analytical Methods, 2016, accepted.

## Slide 45
Benchtop DART-Single Quadrupole MS
Bernier et al., Analytical Methods, 2016, submitted.

## Slide 46
DART-QDa “Fingerprinting” of Various Fake “Recipes”

## Slide 47
PCA Scores Plot of “DART Fingerprints”

## Slide 48
Snyder, D.T., Pulliam, C. J., Ouyang, Z., Cooks, R. G., Miniature and Fieldable Mass Spectrometers: Recent Advances, Anal. Chem., 2016, 68, 2-29
Yang, M.; Kim, T. Y.; Hwang, H. C.; Yi, S. K.; Kim, D. H. J. Am. Soc. Mass Spectrom. 2008, 19, 1442−1448.
www.908devices.com
Miniature Mass Spectrometry

## Slide 49: Summary
No single analytical technique provides enough information to confirm that a drug is genuine. It is usually best to work through tests beginning with the easiest or least expensive ones. Only if samples pass these tests should the inspector move on to more difficult or expensive ones.
An understanding of the technological landscape, the range and gaps in available technologies, and the likely improvements in the near future, is essential for using technologies in developing countries.
Efforts should be focused on developing a central repository for existing and newly innovative detection, sampling, and analytical technologies.
IOM “Countering the Problem of Falsified and Substandard Drugs”, 2013.

## Slide 50
Thank you!
Fernández group:
  Maru Monge, Julia Culzoni, Dana Hostetler, Christina Y. Hampton, Krystyn Alter-Hall, Leonard Nyadong, Glenn Harris, Prabha Dwivedi, Manshui Zhou
Prof. Paul Newton, Oxford
NSF CAREER Award
NSF MRI Instrument Develop
NSF-NASA Center for Chemical Evolution (Instrument Access)
Bill and Melinda Gates Foundation-ACT Consortium
WHO (WPRO)
US Pharmacopeia Fellowships
Global Fund